## Slide 1: Three scenarios proposed to NURC for joint experiments in La Spezia in 2012
Folklore: no answer received, yet, despite the multiple pings 

## Slide 2: Experiment 1: USR and fixed routes
USR: link error control protocol for underwater networks based on selective repeat

## Slide 3: Experiment 1: USR and fixed routes

## Slide 4: Experiment 1: USR and fixed routes
Objective
  Measure the throughput, packet error rate and in-order delivery delay
  Possibly compare against a protocol with simpler or no error control

## Slide 5: Experiment 2: UW-DTN
UW-DTN
  A protocol to exchange data between mobile assets in a store-and-forward fashion
Basics
  4-way handshake to exchange “interests”
  Ensuing packet exchange makes use of the USR protocol
Objective of UW-DTN
  Provide a means for mobiles to forward data to a static sink in a network with erratic connectivity

## Slide 6: Experiment 2: UW-DTN in operation

## Slide 7: Experiment 2: objectives
Measure how fast the data about the mobile assets reaches the sink
At any given time, measure old the sink’s data about any asset is
Measure the probability of losing packets (delivery timeout, full buffer at the transmitter)

## Slide 8: Experiment 3: UW-Polling
UW-Polling
  A protocol for allowing an AUV to coordinate a set of nodes and retrieve data using controlled access

## Slide 9: Experiment 3: UW-Polling

## Slide 10: Experiment 3: UW-Polling
Objectives
  Evaluate the performance of UW-Polling in terms of packet error rate
  Possibly compare the performance of UW-Polling against the performance of other MAC protocols (e.g., DACAP)